## Slide 1: Stimulus Opto-Mechanical
ALAR-100; AVS125; ATS03005
ANT-50-95L
MAX343
ATS100-200
Pupil Masks
DM
Source
Telescope focus

## Slide 2: Stimulus Insertion
Initial fold translates to insert stimulus or allow telescope beam to pass
  Aerotech ATS100-200, 8” travel
  Final collimating lens will travel with this as well due to space constraints

## Slide 3: Sources
Single mode fiber
White light source (Ocean, CVI)
  Filters in source before fiber coupling
Laser option for alignment
  Manual fiber swap
3 axis stage for tip/tilt/focus image control
  Thorlabs MAX343, 4mm travel per axis, 60nm resolution

## Slide 4: Pupils
DM Pupil
  14.5mm full telescope, 7.7mm DM
  Translate between DM and 25mm flat
    Aerotech ANT-50-95L, 50mm travel, 5nm resolution
Pupil for masks
  60mm
  Full rotation, X-Y positioning
    Aerotech ALAR rotation stage, 100mm CA
    Aerotech AVSI125 (lift/y-axis), 25mm travel, 0.5um resolution
    Aerotech ATS03005 (x-axis), 50mm travel, 0.12um resolution